## Slide 1: GLM Laser Beacon Activities
GLM Science Meeting, Huntsville AL
September 12, 2017
Dennis Buechler, NASA/MSFC
(other team members)

## Slide 2
Use laser beacons as well characterized signals to evaluate GLM geolocation accuracy
  Laser locations are well characterized (within few mm)
  Lasers tuned to near 777.4 nm wavelength
  Two lasers to provide large baseline
    Greenbelt, MD
    Monument Peak, CA
  The lasers are pulsed (50 Hz or 100 Hz) so GLM events are processed as lightning by the Ground Processing Algorithm
    The GPA will geolocate the laser signal
    The laser location is well known and can be compared to the GPA derived geolocation
    GLM geolocation requirement 5 km (MRD)
  Examine diurnal changes in geolocation accuracy
GLM Laser Beacons

## Slide 3
Laser Beacon Locations

## Slide 4: GOES-16 Laser Operations
Date | Time (UTC) | Location GB-Greenbelt MP-Monument Pk | Notes
April 19, 2017 | 0152-0352 | GB | 
April 29, 2017 | 0055-0200 | GB | 
May 3, 2017 | 1720-1850 | GB | dither
May 8, 2017 | 1730-1840 | GB | 
June 9, 2017 | 1645-1710 | GB | 
June 11, 2017 | 0300-0340 | GB | 
June 13, 2017 | 1700-1712 | GB | dither
June 24, 2017 | 0420-0510 | MP | 
June 28, 2017 | 1750-1754 | GB | Very few events
July 13, 2017 | 0339-0715 | GB & MP | 
Aug 10, 2017 | 0225-0323 1440-1552 | GB & MP GB & MP | Night Day
Sep 5, 2017 | 1405-1455 | GB & MP | 

## Slide 5: GOES-16 Laser Operations (continued)
Date | Time (UTC) | Location GB-Greenbelt MP-Monument Pk | Notes
Sep 21, 2017 | 1450-1655 1850-1830 | GB & MP GB & MP | 
Oct 2-3, 2017 | 1020/2-1409/3 | GB & MP | 24 hr test (hourly obs)
Nov 28, 2017 | 0340-0425 | GB | 
Nov 29, 2017 | 0250-0320 2149-2215 | GB & MP GB & MP | 
Nov 30, 2017 | 0350-0415 | GB & MP | 
Dec 19, 2017 | 2115-2130 2200-2240 | MP GB & MP | At 75.2° W
Dec 20 , 2017 | 0010-0045 0155-0225 | GB & MP GB & MP | 
Jan 5, 2018 | 0018-0040 2250-2328 | GB GB & MP | 
Jan 6, 2018 | 0210-0240 | GB & MP | 
Jan 17, 2018 | 2225-2255 | MP | @ GOES-E Prior to PS-PVR
Jan 18, 2018 | 0150-0210 0445-0515 | GB & MP GB & MP | INR optimized

## Slide 6: GOES-16 24 Hr Test 2-3 Oct 2017

## Slide 7
GOES-16 Laser Test 3

## Slide 8
GOES-16 Laser Test 3
Events

## Slide 9
GOES-16 Laser Test 3
Groups

## Slide 10
GOES-16 Laser Test 3
Flashes

## Slide 11
Date | Time (UTC) | Monument Peak | Greenbelt
Jan 17, 2018 | 2225-2255 | 2.86 | ----
Jan 18, 2018 | 0150-0210 | 2.64 | 4.38
Jan 18, 2018 | 0445-0515 | 0.63 | 1.84
GOES-16 GLM
Geolocation Offsets

## Slide 12
GOES-17 Initial Laser Beacon Tests

## Slide 13
GOES-17 Laser Tests
NOAA's GOES-17 satellite has not been declared operational and its data are preliminary and undergoing testing. Users receiving these data through any dissemination means (including, but not limited to, PDA and GRB) assume all risk related to their use of GOES-17 data and NOAA disclaims any and all warranties, whether express or implied, including (without limitation) any implied warranties of merchantability or fitness for a particular purpose.

## Slide 14
GOES-17 Laser Test (GB)
Events
NOAA's GOES-17 satellite has not been declared operational and its data are preliminary and undergoing testing. Users receiving these data through any dissemination means (including, but not limited to, PDA and GRB) assume all risk related to their use of GOES-17 data and NOAA disclaims any and all warranties, whether express or implied, including (without limitation) any implied warranties of merchantability or fitness for a particular purpose.

## Slide 15
GOES-17 Laser Test (GB)
Flashes
NOAA's GOES-17 satellite has not been declared operational and its data are preliminary and undergoing testing. Users receiving these data through any dissemination means (including, but not limited to, PDA and GRB) assume all risk related to their use of GOES-17 data and NOAA disclaims any and all warranties, whether express or implied, including (without limitation) any implied warranties of merchantability or fitness for a particular purpose.

## Slide 16
GOES-17 Laser Test (MP)
NOAA's GOES-17 satellite has not been declared operational and its data are preliminary and undergoing testing. Users receiving these data through any dissemination means (including, but not limited to, PDA and GRB) assume all risk related to their use of GOES-17 data and NOAA disclaims any and all warranties, whether express or implied, including (without limitation) any implied warranties of merchantability or fitness for a particular purpose.

## Slide 17
GOES-17 Laser Test (MP)
Flashes
NOAA's GOES-17 satellite has not been declared operational and its data are preliminary and undergoing testing. Users receiving these data through any dissemination means (including, but not limited to, PDA and GRB) assume all risk related to their use of GOES-17 data and NOAA disclaims any and all warranties, whether express or implied, including (without limitation) any implied warranties of merchantability or fitness for a particular purpose.

## Slide 18
Future Laser Tests
GOES-16/17 Comparison
  Can accomplish GOES-17 geolocation goals while comparing with GOES-16 with current GPA updates
  Laser on one satellite for 5-15 min then on the other for 5-15 min
  Compare other GLM parameters (geolocation, energy, overshoot correction)
Test 1: Pre yaw flip (24 Sep 2018)
  Test procedure for three different times
  Different CCD pixels than post yaw flip
Test 2: 24 hour test
  Examine diurnal geolocation accuracy
Test 3: After GOES-17 drift (only at Monument Peak)
  Baseline measurements at GOES-W

## Slide 19: Laser Beacon Animations
GOES-16 Laser Beacon Test 13 July 2017
13 July 2017 (GLM data over ABI IR image):
Times are not synched up in animations
Note effect of clouds on Greenbelt performance

## Slide 21
GOES-16 Laser Test 2 2

## Slide 22
GOES-16 Laser Test 2
Events

## Slide 23
GOES-16 Laser Test 2
Groups

## Slide 24
GOES-16 Laser Test 2
Flashes

## Slide 25
The SLR Satellite Ranging Group has a number of installations
  Tracking/locating satellites
Identified and procured lasers based on GLM detection methodology
  Wavelength near 777.4 nm
  Pulse width ~1.5 ms
  50 Hz
  Sufficient power at GLM
Installed and mounted lasers on existing mounts
Developed test procedures and procured safety approvals
Tested that GLM detected laser signal
Trained crews to run the laser beacon tests
Satellite Laser Ranging Group

## Slide 26
Schedule date
Notify NOAA so notifications can be sent out
Monitor weather conditions at sites
Morning of test confirm go/no go
  Weather
  Personnel
  Data availability
Start web tool for monitoring test
  Hosted on the GOES-R Field campaign web site
Laser Beacon Test Procedure

## Slide 27: Laser Operations
Date | Time (UTC) | Location GB-Greenbelt MP-Monument Pk | Notes
April 19, 2017 | 0152-0352 | GB | 
April 29, 2017 | 0055-0200 | GB | 
May 3, 2017 | 1720-1850 | GB | dither
May 8, 2017 | 1730-1840 | GB | 
June 9, 2017 | 1645-1710 | GB | 
June 11, 2017 | 0300-0340 | GB | 
June 13, 2017 | 1700-1712 | GB | dither
June 24, 2017 | 0420-0510 | MP | 
June 28, 2017 | 1750-1754 | GB | Very few events
July 13, 2017 | 0339-0715 | GB & MP | 
Aug 10, 2017 | 0225-0323 | GB & MP | Night drift
Aug 10, 2017 | 1440-1552 | GB & MP | Day, drift
Sep 6, 2017 | 1405-1455 | GB & MP | 

## Slide 28
Laser Beacon Web Display
Uses GLM L2 PDA data from the GHRC
IDL tool
  Monitors when new GLM L2 file is available
  Plots image of last 4 minutes of GLM data around the laser locations
  Updates image when new L2 file comes in
GHRC developed tool loads the image onto web page
Latency generally varies from 1.5 to 2.5 minutes

## Slide 29
Laser Beacon Web Example

## Slide 30
Lightning Web Example

## Slide 31
Laser Beacon Time Series

## Slide 32
Laser Beacon Events (OE)

## Slide 33
Dither Time Series

## Slide 34
Dither Events

## Slide 35
Dither Groups

## Slide 36
Dither Flashes

## Slide 37
LM Geolocation
GLM events computed using LM algorithms
  Located to surface
  10 Aug 2017

## Slide 38
Demonstrated that laser beacons can be safely used as a proxy for GLM lightning
Successful development of web based realtime feedback
Observed offset between laser location and GLM geolocation
Laser Beacon Summary

## Slide 39
Continue comparisons with GLM L2 data
  Examine parallax corrections
Continue geolocation analysis
  apply latest overshoot corrections
  Apply latest geolocation parameters
Conduct a 24 hour test to examine diurnal changes in geolocation
Lasers will be visible to GLM when in East position
GOES-S will have fewer coastlines for navigation
Laser Beacon

## Slide 41
Laser Beacon Groups (OE)

## Slide 42
Laser Beacon Flashes (OE)

## Slide 43
GOES-17 Laser Test (MP)
Groups
NOAA's GOES-17 satellite has not been declared operational and its data are preliminary and undergoing testing. Users receiving these data through any dissemination means (including, but not limited to, PDA and GRB) assume all risk related to their use of GOES-17 data and NOAA disclaims any and all warranties, whether express or implied, including (without limitation) any implied warranties of merchantability or fitness for a particular purpose.