## Slide 1: GLM validation over southern Canada using CLDN and SOLMA: - “Final” Results -
2018 GLM Annual Science Team Meeting
Huntsville, AL
David Sills, Hong Lin, Brian Greaves, Helen Yang
S&T / MSC, ECCC
12 Sep 2018

## Slide 2: Outline
Canadian Context
  Data sources
  GLM validation strategy
  Limitations
Methods
  ‘Deep dives’ in four domains
  Choice of matching thresholds
Results
  DE results relative to CLDN / SOLMA
  Case studies by domain
Summary
  Acknowledgments

## Slide 3: Data Sources
GLM
  GOES-16 (2018)
CLDN (NALDN)
  84-station network (ECCC/Vaisala)
  CG and IC data
SOLMA
  14-station array (ECCC)
  Toronto area
ECCC Radar
  Echo top data

## Slide 4: GLM Validation at ECCC
NOAA–ECCC MOU re GLM collaboration:
  Leads Steve Goodman / Dave Sills
  Task 1: GLM on-orbit validation and product characterization over Canada
    Provide SOLMA ‘supersite’ data to cal/val team
    ECCC GLM Validation Project to ensure GLM data are reliable, high-quality, need to answer the following questions:
    What are the limitations to the use of GLM data in the Canadian context?
    How accurate are GLM observations in space and time?
    What is the detection efficiency over Canada relative to CLDN and SOLMA?

## Slide 5: GLM – Canadian Context
Limitations over Canada:
Resolution – 8 km at nadir but coverage over Canada has ~9-14 km resolution, with most areas near ~10 km resolution

## Slide 6: GLM – Canadian Context
Limitations over Canada:
Resolution – 8 km at nadir but coverage over Canada has ~9-14 km resolution, with most areas near ~10 km resolution
Parallax issues
  Storm view increasingly side versus top as latitude increases, seen as low top
  Geo-location uses cloud top height model
GLM
GLM Subpoint

## Slide 7
GLM
GLM Subpoint
Surface of Earth
12 km cloud top
Model location offset for 12 km
To GLM satellite
Assuming 45⁰N latitude…

## Slide 8
GLM
GLM Subpoint
15 km cloud top
Shifted north
~3 km
Surface of Earth
To GLM satellite
Model location offset for 12 km
Assuming 45⁰N latitude…

## Slide 9
GLM
GLM Subpoint
Surface of Earth
10 km cloud top
To GLM satellite
Shifted south ~2 km
Model location offset for 12 km
Assuming 45⁰N latitude…

## Slide 10
GLM
GLM Subpoint
Surface of Earth
6 km cloud side
To GLM satellite
Shifted south ~6 km
Model location offset for 12 km
Assuming 45⁰N latitude…

## Slide 11
Surface of Earth
6 km cloud side
To GLM satellite
Shifted south ~6 km
Model location offset for 12 km
Great Lakes lake-effect snow (with lightning) has very low cloud tops (4-6 km)
Assuming 45⁰N latitude…

## Slide 12: GLM Validation Plan – ‘Deep Dives’
Spirit River, AB 55.7N, 119.2W
Holyrood, NL
47.3N, 53.2W
Woodlands, MB 50.2N, 97.8W
Toronto, ON 43.7N, 79.6W
(SOLMA)
1 SOLMA + CLDN site with radar coverage – Toronto
3 CLDN-only sites with radar coverage – W, central, E
Courtesy NOAA

## Slide 13: Methods – Matching Thresholds
Relative Detection Efficiencies
Using CLDN and GLM flashes over active 6-hr periods
Increased time and distance thresholds until no significant change in matches
Result: 0.5 s and 20 km radius
20 km
4 May 2018
4 May 2018
0.5 s

## Slide 14
West
Central
South
East
16 Cases Total

## Slide 15
CLDN > SOLMA > GLM-16
CLDN / GLM-16
SOLMA / GLM-16
SOLMA / CLDN

## Slide 16: WEST – 20 May 2018 @ Holyrood, NL
Weak storms
Low echo tops 6-8 km
GLM displacement ~10 km towards subpoint (to SE)
50 km
GLM >> CLDN
Evening
20:30 LT 0230 UTC
10-min period

## Slide 17: CENTRAL – 14 June 2018 @ Woodlands, MB
Supercells with baseball hail
High echo tops 12-19 km
GLM displacement ~6 km away from subpoint (to NW)
50 km
Evening 17:00 LT 2300 UTC
10-min period
No GLM!
‘optical extension’?

## Slide 18: SOUTH – 16 Jul 2018 @ Toronto, ON
Weak storms
Echo tops 8-12 km
GLM displacement ~1 km toward subpoint (to S)
50 km
GLM >> CLDN
Daytime 13:00 LT 1700 UTC
10-min period

## Slide 19: SOUTH – 16 Jul 2018 @ Toronto, ON
Weak storms
Echo tops 8-12 km
GLM displacement ~1 km toward subpoint (to S)
50 km
GLM >> CLDN
Daytime 13:00 LT 1700 UTC
10-min period

## Slide 20: EAST – 30 Jul 2018 @ Holyrood, NL
Weak storms
Echo tops 10-12 km
GLM displacement ~5 km toward subpoint (to SW)
50 km
GLM >> CLDN
Daytime 15:30 LT 1900 UTC
10-min period

## Slide 21: SOUTH - Single Visible CG Flash
6 Sep 2018 N of Toronto
Nighttime (~10 PM local)
Northern edge of LMA
Low echo top ~9 km
SOLMA: one 0.7s flash
CLDN: six single-stroke flashes (-CG, 5 IC)
GLM: one 0.7s flash, 49 groups, 182 events
Time
Vertical
Vertical
Plan View
Visual CG

## Slide 22: Single Flash – SOLMA
Dashcam
SOLMA sources
SOLMA CG
12 km

## Slide 23: Single Flash – CLDN
Dashcam
CLDN ICs
CLDN -CG
12 km

## Slide 24: Single Flash – GLM
Dashcam
GLM flash
GLM events
12 km

## Slide 25: Single Flash Comparison
Dashcam
SOLMA CG
CLDN -CG
GLM flash
GLM ~11 km to SSW
(part parallax / part side of cloud)
12 km

## Slide 26: Summary
ECCC validation plan focused on ‘deep dives’ in four domains across Canada
Results:
  GLM DE relative to CLDN varies with location but generally ~70% on average
  GLM DE relative to SOLMA lower, ~50% on average (need to investigate further…)
  Overly simple cloud height model results in displacements – improvement in works
  Side of cloud displacements / ‘optical extension’ / excessive CLDN IC flash artifacts are concerns
Future work:
  Compare GOES-17 GLM data

## Slide 27: Acknowledgments
GLM: Emma Hung, Aiming Wu, Ron Goodson, Arne Alfheim
SOLMA: Paul Krehbiel, Bill Rison, Dan Rodeheffer, Ron Thomas, Reno Sit, Michael Harwood, Karen Haynes, Rob Reed, Larry Dusolt, Emma Hung, Paul Joe, Diane Johnston, John MacPhee
CLDN: Lyn Mainwaring, Ted Gresiuk

## Slide 28: Summary
ECCC validation plan focused on ‘deep dives’ in four domains across Canada
Results:
  GLM DE relative to CLDN varies with location but generally ~70% on average
  GLM DE relative to SOLMA lower, ~50% on average (need to investigate further…)
  Overly simple cloud height model results in displacements – improvement in works
  Side of cloud displacements / ‘optical extension’ / excessive CLDN IC flash artifacts are concerns
Future work:
  Compare GOES-17 GLM data
Thanks! David.Sills@canada.ca